## Slide 1
《计算思维与系统设计基础》 第二讲
从逻辑符号到算数系统
主讲老师：顧學雍
课程助教：侯煜欣、孙喆、林东生
课程wiki主页：toyhouse.cc
2016年秋 周四 19：20~21：50
地点：第六教学楼A113

## Slide 2
效果
输出
过程
输入
目标
背景
外部因素
逻辑模型-课程的设计合约
课堂讲解
toyhouse.cc Wiki-based Knowledge Collection System
Gitlab 服务
Nand2Tetris Software
参考书目：Test Driven Development with Python
安装Django, Tensorflow等软件
辕询提供的软件范例
  Painting in HTML5
  PHP-based Blockchain code
通过对ALU, Godel Number的介绍，解释为何图灵计算机具备万用的计算能力
展示围棋与Cellular Automata、逻辑电路的类比对应关系，介绍这些系统为何能做成具有图灵完备性的计算机。
to ”Software”, so that students can experience how layers of languages interact
根据这周的内容，开始撰写一个开发围棋系统的团队任务逻辑模型
每个人完成前week1的Nand2Tetris课中的HDL电路设计，上传源代码到GitLab项目中。
安装Python, Eclipse, NetLogo, Mathematica, PHP等软件开发工具
用逻辑化的形式语言（伪代码，或是Python, Mathematica的逻辑判断式）撰写围棋的下棋规则
每周Wiki上的团队与个人学习报告
各小组开始为本学期的各项任务撰写逻辑模型
了解如何用Nand或Nor闸门，实现MUX，并通过HDL Simulation的测试脚本
了解二进位的数字表达方式，并知道多位二进位的加法运算器的组成元素为何
了解ALU是计算机中唯一对运算任务执行者，所有的运算，不论是符号处理，或是数字处理，都是经由ALU的函数来完成。其他的元件都是储存或通信的功能。
解释如何用逻辑符号运算的方式实现算数系统的功能，其限制为何？
Multiplexer (MUX)是一种选择电路功能（函数）的机制，可用于通信、选择逻辑分枝条件、函数切换等场景
何谓函数？介绍ALU，Arithmetic Logic Unit，这是一种万用函数。介绍Godel Number与形式化语言的关系
计算思维是一个基于可经由形式化语言描述目标与可经由逻辑检验条件的思考方式
逻辑模型是用自然语言描述的形式化设计合约
工程系统的开发，应该从设计合约出发，（Nand2Tetris提供了一套学习计算机架构用的全栈测试与仿真系统）
学生们在安装各种工具可能碰到不同的技术问题，造成进度落后
同学们在完成个别任务之后，没有从整个项目的系统角度思考任务之间的联系，造成前后工作不易衔接
只偏重抽象理论，或是只专注于技术细节，故而未能储备足够的知识去体会系统设计的全局性视角

## Slide 3
第一周回顾: Design by Contract 基于（逻辑）合约的设计
内容:
系统的可信度，来自通过设计合约的程度 Trust worthiness is based on Design Contract
根据真值表决定设计是否合格 Truth Table is the Contract for Logic Circuit Design
  课上汇报：各小组把我上周用英文写的逻辑模型翻译成中文的版本
复杂性来自简单元件的链接关系 Complexity comes from the connections of simple things
  You should be watching Nand2Tetris and Computational Structure’s first week video
  Learn the whole stack by building a Blockchain-recorded Go game

## Slide 4
01
01
课程背景

## Slide 5
  一个形式化语言实现一种计算模型
The era of Super-Human Intelligence
  The classification of intelligence is determined by the use of Languages
  Formal Languages has computable objects: Vocabulary, Grammar, Semantics
From Logics to Number Systems: The Workhorse of Turing Complete Computation: Arithmetic Logic Unit
Memory: The Space-Time Entanglement of Digital Circuitry
Composition: The idea behind the assembly language
  From Binary Notation to Human Mnemonics

## Slide 6
现代计算系统是多层形式化语言的迭代结构
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12
(Abstraction–implementation paradigm)

## Slide 7: Tools and Books are freely available for building complex systems
http://chimera.labs.oreilly.com/books/1234000000754/index.html

## Slide 8
模块化项目 + 自动检验工具

## Slide 9
Given: Nand(a,b), false
We can build:
Not(a) = Nand(a,a)
true = Not(false)
And(a,b) = Not(Nand(a,b))
Or(a,b) = Not(And(Not(a),Not(b)))
Xor(a,b) = Or(And(a,Not(b)),And(Not(a),b)))
Etc.
George Boole, 1815-1864
(“A Calculus of Logic”)
極限學習過程
  Boolean algebra

## Slide 10
Xor(a,b) = Or(And(a,Not(b)),And(Not(a),b)))
Implementation
Interface
Claude Shannon, 1916-2001
(“Symbolic Analysis of Relay and Switching Circuits” )
極限學習過程
  Gate logic

## Slide 11
Gate logic – a gate architecture designed to implement a Boolean function
Elementary gates:
Composite gates:
Important distinction: Interface (what) VS implementation (how).
極限學習過程
  Gate logic

## Slide 12
From a computer science perspective, physical realizations of logic gates are irrelevant.
極限學習過程
Circuit implementations

## Slide 13
Proposed Implementation: based on Not, And, Or gates.
a b sel out
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1
sel out
0 a
1 b
極限學習過程
  Multiplexer

## Slide 14
a b out
0 0 0
0 1 0
1 0 0
1 1 1
And.cmp
load And.hdl,
output-file And.out,
compare-to And.cmp,
output-list a b out;
set a 0,set b 0,eval,output;
set a 0,set b 1,eval,output;
set a 1,set b 0,eval,output;
set a 1, set b 1, eval, output;
And.tst
And.hdl
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
Contract:
When running your .hdl on our .tst, your .out should be the same as our .cmp.
極限學習過程
  Example: Building an And gate

## Slide 15
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
Interface: And(a,b) = 1 exactly when a=b=1
極限學習過程
  Building an And gate

## Slide 16
Implementation: And(a,b) = Not(Nand(a,b))
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
極限學習過程
  Building an And gate

## Slide 17
Implementation: And(a,b) = Not(Nand(a,b))
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
極限學習過程
  Building an And gate

## Slide 18
CHIP And
{ IN a, b;
OUT out;
Nand(a = a, b = b, out = x);
Not(in = x, out = out)
}
Implementation: And(a,b) = Not(Nand(a,b))
And.hdl
極限學習過程
  Building an And gate

## Slide 19
test script
HDL program
極限學習過程
  Hardware simulator (demonstrating Xor gate construction)

## Slide 20: Counting systems
quantity decimal binary 3-bit register
0 0 000
 1 1 001
 2 10 010
 3 11 011
 4 100 100
 5 101 101
 6 110 110
 7 111 111
 8 1000 overflow
 9 1001 overflow
 10 1010 overflow

## Slide 21: Rationale

## Slide 22
no overflow
overflow
Algorithm: exactly the same as in decimal addition
Overflow (MSB carry) has to be dealt with.
Binary addition
Assuming a 4-bit system:
0 0 0 1
1 0 0 1
0 1 0 1
0 1 1 1 0
+
1 1 1 1
1 0 1 1
0 1 1 1
1 0 0 1 0
+

## Slide 23: Representing negative numbers (4-bit system)
The codes of all positive numbers begin with a “0”
The codes of all negative numbers begin with a “1“
To convert a number: leave all trailing 0’s and first 1 intact, and flip all the remaining bits
0 0000
1 0001 1111 -1
2 0010 1110 -2
3 0011 1101 -3
4 0100 1100 -4
5 0101 1011 -5
6 0110 1010 -6
7 0111 1001 -7
1000 -8
Example: 2 - 5 = 2 + (-5) = 0 0 1 0
+ 1 0 1 1
1 1 0 1 = -3

## Slide 24: Building an Adder chip
Adder: a chip designed to add two integers
Proposed implementation:
  Half adder: designed to add 2 bits
  Full adder: designed to add 3 bits
  Adder: designed to add two n-bit numbers.

## Slide 25: Half adder (designed to add 2 bits)
Implementation: based on two gates that you’ve seen before.
a b sum carry
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1

## Slide 26: Full adder (designed to add 3 bits)
Implementation: can be based on half-adder gates.
a b c sum carry
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1

## Slide 27: n-bit Adder (designed to add two 16-bit numbers)
Implementation: array of full-adder gates.
... 1 0 1 1 a
… 0 0 1 0 b
… 1 1 0 1 out
+

## Slide 28: The ALU (of the Hack platform)
out(x, y, control bits) =
x+y, x-y, y–x,
0, 1, -1,
x, y, -x, -y,
x!, y!,
x+1, y+1, x-1, y-1,
x&y, x|y

## Slide 29: ALU logic (Hack platform)
Implementation: build a logic gate architecture that “executes” the control bit “instructions”: if zx==1 then set x to 0 (bit-wise), etc.

## Slide 30
The ALU in the CPU context (a sneak preview of the Hack platform)
ALU
Mux
D
out
A/M
a
D register
A register
A
M
c1,c2, … ,c6
RAM
(selected register)

## Slide 31: Perspective
Combinational logic
Our adder design is very basic: no parallelism
It pays to optimize adders
Our ALU is also very basic: no multiplication, no division
Where is the seat of more advanced math operations? a typical hardware/software tradeoff.

## Slide 32
  CPU 是一种图灵完备的计算单元
http://www.visual6502.org/JSSim/index.html
https://en.wikipedia.org/wiki/MOS_Technology_6502

## Slide 33: Historical end-note: Leibnitz (1646-1716)
“The binary system may be used in place of the decimal system; express all numbers by unity and by nothing”
1679: built a mechanical calculator (+, -, *, /)
CHALLENGE: “All who are occupied with the reading or writing of scientific literature have assuredly very often felt the want of a common scientific language, and regretted the great loss of time and trouble caused by the multiplicity of languages employed in scientific literature:
SOLUTION: “Characteristica Universalis”: a universal, formal, and decidable language of reasoning
The dream’s end: Turing and Gödel in 1930’s.
Leibniz’s medallion for the Duke of Brunswick

## Slide 34: Gödel Numbering
In mathematical logic, a Gödel numbering is a function that assigns to each symbol and well-formed formula of some formal language a unique natural number, called its Gödel number. The concept was used by Kurt Gödel for the proof of his incompleteness theorems. (Gödel 1931)
  https://en.wikipedia.org/wiki/G%C3%B6del_numbering#CITEREFG.C3.B6del1931
Kurt Gödel’s picture from Wikipedia

## Slide 35: Cellular Automata
A cellular automaton (pl. cellular automata, abbrev. CA) is a discrete model studied in computability theory, mathematics, physics, complexity science, theoretical biology and microstructure modeling. Cellular automata are also called cellular spaces, tessellation automata, homogeneous structures, cellular structures, tessellation structures, and iterative arrays.
  https://en.wikipedia.org/wiki/Cellular_automaton
John Horton Conway
Picture from Wikipedia
Cellular Automaton picture from Wikipedia

## Slide 36
Application level: Go (by: José Luis Gómez-Muñoz)

## Slide 37
Your ability in identifying proper reference material
  Learn from the Internet and Public Libraries
  Use relevant data sources and provide argument for its validity
Your interpretation of content
  Reflected in your documentation and implementation of the Go System
The quantity and quality of efforts expended in reviewing your own work.
  Reflected by wiki and Git process data
  课程分数的评价

## Slide 38
極限學習過程
其他信息
如果关于课程、认知基础等问题有任何疑惑、想法、灵感，欢迎用任何方式联系我们。
孙一乔
Email：sunvianet@foxmail.com
微信：18210130968
电话：18210130968
办公室：李兆基科技大楼B559
顾学雍
Email：benkoo@mail.tsinghua.edu.cn
微信：koo0905
办公室：李兆基科技大楼B572

## Slide 39
THANK YOU !